XInC2 Dev 2
Perf Spec
Adam Gulyas
January 15, 2021

---
General Info
2021-01-07
The target audiences are university capstone groups and hobbyists.
Design choices will heavily weight compatibility with Arduino and Raspberry Pi ecosystems.
If possible, PCB design will be two layer, single sided.
PCB will be able to populate either EEPROM or Flash memory ICs through the use of common footprints and pin outs. Compatible part numbers for each type will be identified.

---
Proposed Format
General board format will follow the below examples:
Programmer at the top
uC bottom center
GPIO around the edge
A few buttons and LEDs

---
Rough PCB Layout
No crystal pulling. Let the user use TMRB for something else.
Block Diagram
Rough PCB Layout
USB
Type C
XPD3
components
Lin. Reg.
USB
Type C
Data
XPD3
RC Clk
RST
BTN
crystal
Flash or
EEPROM*
5V
SPI
XInC2
Lin.
Reg.
3.3V
XInC2
RC Clk
24.576 MHz
Crystal**
3 colour
LED
From XInC2 datasheet: The preliminary maximum clock speed at 3.3V for commercial conditions is 100MHz.”
RGB
LED
* Either population option possible
** Use a common crystal footprint to enable using other frequencies
2x button
RST button
Header
2x buttons
Header